## Slide 1: 081100M01002H 图像处理与分析 第二讲: 视觉与图像 (II) 成像与采样，彩色图像，数字图像处理的基本概念
Lecture 2 September 12, 2019

## Slide 2: 第一讲：部分代表性提问与回答
机器视觉与计算机视觉的区别是什么？ - 通常在工业场景下的计算机视觉被称为机器视觉 - 在工业场景下成像条件经常可控
本课程需要的数学基础是什么？如何准备？ - 线性代数，微积分，概率论 （参考Gonzalez第二章） - Justin Solomon 的讲义，非课程要求，仅供参考
http://people.csail.mit.edu/jsolomon/
如何才能学会做图像处理算法？ - 针对一个图像处理问题建立合理的数学模型，进而 对模型采用数值/优化方法进行求解

## Slide 3: 内容提纲
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 4
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 5: 图像格式示例: PBM/PGM/PPM
PBM: portable bitmap format
PGM: portable graymap format
PPM: portable pixmap format
Magic Number | Type | Encoding
P1 | Portable bitmap | ASCII
P2 | Portable graymap | ASCII
P3 | Portable pixmap | ASCII
P4 | Portable bitmap | Binary
P5 | Portable graymap | Binary
P6 | Portable pixmap | Binary
http://en.wikipedia.org/wiki/Netpbm_format

## Slide 6: 例 1: PBM
http://en.wikipedia.org/wiki/Netpbm_format

## Slide 7: 例 2: PGM
http://en.wikipedia.org/wiki/Netpbm_format

## Slide 8: 例 3: PPM
http://en.wikipedia.org/wiki/Netpbm_format

## Slide 9: 文件格式示例：TIFF-Tagged Image File Format
TIFF 是一种常用无损图像格式
https://www.adobe.io/open/standards/TIFF.html 最新版: TIFF 6.0 (1992), TIFF Supplement 2 (2002)
其他常见的图像格式包括：bmp, jpeg, gif, png等等 https://helpx.adobe.com/hk_en/photoshop/using/file-formats.html
各种图像格式之间通常可以自由转换
实际应用中经常连带存储关于成像条件的metadata(元数据)

## Slide 10: 文件格式示例：JPEG-Joint Photographic Experts Group
正式标准于1992年发布，最新一次修订于2012。早期核心专利来自IBM和Mitsubishi Electric。
广泛应用于数字相机图像和互联网图像，采用有损压缩，通常压缩比可达10:1, 节省文件存储空间。
不适于一些特定类型的图像如线条图像。
2002-2013 年间专利纠纷部分限制了其应用。
https://en.wikipedia.org/wiki/JPEG

## Slide 11: MATLAB图像读写与显示函数
读写函数：imread, imwrite
显示函数：imshow
> img = imread(‘mandril_color.tif’); > imshow(img, [ ]); > imwrite(img, ‘tiff’,’compression’,’none’);
mandril_color.tif

## Slide 12
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 13: 数字图像采集典型场景示例 I

## Slide 14: 数字图像采集典型场景示例 II

## Slide 15: 典型成像设备设置 (I)

## Slide 16: 典型成像设备设置 (II)

## Slide 17: 常用成像设备：CCD (电荷耦合器件）
http://micro.magnet.fsu.edu/primer/java/digitalimaging/ccd/interline/index.html

## Slide 18: 常用成像设备：CMOS (互补金属氧化物半导体)
https://www.azom.com/article.aspx?ArticleID=16321
https://www.dpreview.com/news/0671207908/canon-is-now-selling-cmos-image-sensors-including-a-120mp-aps-h-beast

## Slide 19: 像素的位深度 (I)
日常用相机的位深度为8
一般认为，典型条件下人类视觉的归一化灵敏度约为1/256.
HDR10 (high dynamic range) 显示器对应的显示像素深度为10
研究用相机的像素位深度可达16
http://micro.magnet.fsu.edu/primer/java/digitalimaging/ccd/interline/index.html
https://www.monitornerds.com/hdr-monitors-gaming/
Bit Depth | Dynamic Range
8 | 0~255
10 | 0~1023
12 | 0~4095
16 | 0~65535

## Slide 20: 像素的位深度 (II)
https://www.rtings.com/tv/learn/hdr10-vs-dolby-vision

## Slide 21
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 22: 采样与量化 (I)

## Slide 23: 采样与量化 (II)
空间采样与量化由物理像素决定。
灰度采样与量化由模拟-数字转换决定。

## Slide 24: 图像的表示

## Slide 25: 几个相关基本概念
动态范围 (dynamic range) -> [Imin, Imax]
饱和 (saturation)
对比度 (contrast) = Imax/Imin

## Slide 26
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 27: 图像的空间分辨率

## Slide 28: 图像的灰度分辨率

## Slide 29: 图像插值
https://en.wikipedia.org/wiki/Bilinear_interpolation

## Slide 30
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 31: 像素间的基本关系

## Slide 32
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 33: 图像的简单算数运算 (I)

## Slide 34: 图像的简单算数运算 (II)

## Slide 35: 图像的集合与逻辑运算示例 (I)

## Slide 36: 图像的集合与逻辑运算示例 (II)

## Slide 37: 图像的几何变换

## Slide 38: 图像变换分类
变换类型 - 刚体（rigid） - 仿射 （affine） - 射影 （projective） - 分布式 （curved）
变换域 - 局部 - 全局

## Slide 39: 线性算子的基本概念

## Slide 40
图像格式示例
图像获取
图像采样与量化
空间分辨率与灰度分辨率
像素间的基本关系
图像处理的基本数学工具
彩色图像
Notes: As you will see again and again in the class, to understand bioimage informatics depends critically on understanding the biological background of bioimage informatics. This is because bioimage informatics is created to answer biological questions rather than for technological curiosity. If we do not understand the biological questions, we will not be able to understand bioimage informatics. So for this reason we need to build some background knowledge about biology, and specifically for this lecture about cell biology.
For the most part of this course, our discussion on biology will be on a level that will be quite comfortable for you.
After that I will give you some historical perspectives and talk about where does it come from. Then I will discuss the learning objectives that we plan to achieve in this class. And finally I will go through the course syllabus together with you and discuss some details.

## Slide 41: 色彩的基本概念 (I)

## Slide 42: 色彩的基本概念 (II)
人类的锥状感光细胞中65%对于红色敏感，33%对于绿色敏感，只有2%对于蓝色敏感。
国际照明委员会定义 蓝 = 435.8 nm 绿 = 546.1 nm 红 = 700 nm

## Slide 43: 不同颜色的组合
光的原色与二次色
颜料的原色与二次色
三色值系数 x = X/(X+Y+Z) y = Y/(X+Y+Z) z = Z/(X+Y+Z)

## Slide 44: 彩色模型(I): RGB模型
(28)3 = 16,777,216

## Slide 46: CMY 和CMYK模型

## Slide 47: HSI 模型
H: 色调 - 纯度
S: 饱和度 - 白色的稀释度
I: 强度

## Slide 48: 灰度图像转换为伪彩色图像 (I)

## Slide 49: 灰度图像转换为伪彩色图像 (II)

## Slide 50: 伪彩色多通道图像

## Slide 51
彩色图像变换

## Slide 52
彩色图像色调校正

## Slide 53
彩色图像处理示例 (I)

## Slide 54
彩色图像处理示例 (II)

## Slide 55
彩色图像处理示例 (III)

## Slide 56
彩色图像处理示例 (IV)

## Slide 57
Questions?

## Slide 58
关于第一次编程作业的说明

## Slide 59: A Microscope as a Linear System
A light microscope can be considered as a linear system.
A linear system satisfies the following two conditions
- Homogeneity
- Additivity
Homogeneity
Additivity

## Slide 60: How to Characterize a Linear System
A linear system can be characterized by
- Impulse response
- Frequency response
Impulse response of a microscope: point spread function
Frequency response of a microscope: optical transfer function

## Slide 61: Airy Disk
Airy (after George Biddell Airy) disk is the diffraction pattern of a point feature under a circular aperture.
It has the following form
Detailed derivation is given in Born & Wolf, Principles of Optics, 7th ed., pp. 439-441.
J1(x) is a Bessel function of the first kind.

## Slide 62: Microscope Image Formation (I)
Microscope image formation can be modeled as a convolution with the PSF.
http://micro.magnet.fsu.edu/primer/java/mtf/airydisksize/index.html

## Slide 63: Microscope Image Formation (II)
The impulse response of the microscope is called its point spread function (PSF).
The transfer function of a microscope is called its optical transfer function (OTF).
The PSF has the shape of an Airy Disk.

## Slide 64: Numerical Aperture
Numerical aperture (NA) determines microscope resolution and light collection power.
n: refractive index of the medium between the lens and the specimen
: half of the angular aperture

## Slide 65: Different Definition of Light Microscopy Resolution Limit (Demo)
Rayleigh limit
Sparrow limit
http://www.microscopy.fsu.edu/primer/java/imageformation/rayleighdisks/index.html

## Slide 66: Summary: High Resolution Microscopy
Size of cellular features are typically on the scale of a micron or smaller.
To resolve such features require
- Shorter wavelength (electron microscopy) - High numerical aperture (resolution) - High magnification (spatial sampling)